## Slide 1: Quantifying Covertness in Communications Systems
Lucas Rooyakkers

## Slide 2: What is Covert Communications?

## Slide 3: What is Covert Communications?

## Slide 4: What is Covert Communications?

## Slide 5: Also Known As
Low Probability of Detection (LPD)
  Used by Information Theorists
  Often formal, mathematical definition
Low Probability of Intercept (LPI)
  Used by Waveform Designers
  Describes signals that are “hard” to intercept

## Slide 6: Fundamental Limits: Square Root Law
Alice can transmit O(√n) bits for every n channel uses.
Alice and Bob need a pre-shared key of O(√n)

## Slide 7: Fundamental Limits: Square Root Law
Comes from Steganography
Doesn’t grow very fast
Assumes Willie knows everything, except secret key

## Slide 8: Fundamental Limits: Positive Capacity
Alice can transmit O(n) bits when:

## Slide 9: Fundamental Limits: Positive Capacity
Alice can transmit O(n) bits when:
  Willie doesn’t know the noise level exactly
  Jammers are used
  There are public spectrum users

## Slide 10: Public Messages
Alice can hide among public messages
  Willie must filter out every public message to detect Alice
  More public users means lower probability of detection

## Slide 11: Public Messages
Alice can hide within public messages
  Alice mush know structure of public message
  Willie must filter out every public message to detect Alice

## Slide 12: Shadow Networks

## Slide 13: Shadow Networks
O(√n) when using undirected antennae
O(n) with beamforming, directed antennae, MIMO

## Slide 14: Detector Theory: Willie’s Test

## Slide 15: Detector Theory: Willie’s Test
Null Hypothesis: Only Noise
  H0: r(t) = n(t)
Alternative Hypothesis: Alice’s Signal and Noise
  H1: r(t) = n(t) + s(t)

## Slide 16: Detector Theory: Detectors
A detector takes the received signal and outputs a test statistic to be compared to a threshold:

## Slide 17: Detector Theory: Error Types
Type I (False Alarm)
Type II (Missed Detection)

## Slide 18: Optimal Detectors: The Radiometer
Compare measured power to noise estimate
Optimal for completely unknown signal, on an AWGN channel
Struggles with interference

## Slide 19: Optimal Detectors: Matched Filters
Signal properties must be known
Can be used in a bank in parallel

## Slide 20: Cyclostationary Detectors
Checks for periodicity in signals
Best for weak signals in noise
No proven “best” metric

## Slide 21: Cyclostationary Detectors
t
BPSK
CDMA-BPSK
AWGN

## Slide 22: How to Create LPI/LPD Waveforms

## Slide 23: How to Create LPI/LPD Waveforms
Lower the Power (at Willie)

## Slide 24: How to Create LPI/LPD Waveforms
Lower the Power (at Willie)
Spread it out in frequency

## Slide 25: How to Create LPI/LPD Waveforms
Lower the Power (at Willie)
Spread it out in frequency
Make the waveform irregular

## Slide 26: Spread Spectrum
Frequency Hopping (FHSS)
Chirp Spread Spectrum (CSS)
Direct Sequence (DSSS)

## Slide 27: Frequency Hopping Spread Spectrum

## Slide 28: Direct Sequence Spread Spectrum
Multiply signal by spreading sequence
Flattens frequency spectrum

## Slide 29: Chirp Spread Spectrum
Direction and slope can encode information
Immune to Doppler shift

## Slide 30: Chaos Communications
A small change to the initial conditions results in a large change to the output.
Chaos provides an irregular waveform
Presents synchronization issues

## Slide 31: The Situation

## Slide 32: The Situation
Fundamental limits established mathematically

## Slide 33: The Situation
Fundamental limits established mathematically
Several methods of increase “covertness”

## Slide 34: The Situation
Fundamental limits established mathematically
Several methods to increase “covertness”
No way to evaluate covertness

## Slide 35: The Situation
Fundamental limits established mathematically
Several methods of increase “covertness”
No way to evaluate covertness
No way to generate optimal covert protocol

## Slide 36: Thesis Question(s)

## Slide 37: Thesis Question(s)
What detection method(s) can Willie employ to best detect LPI/LPD signals?

## Slide 38: Thesis Question(s)
What detection method(s) can Willie employ to best detect LPI/LPD signals?
Which protocols and techniques can Alice employ to best evade detection (while communicating with Bob with a given probability of error)?

## Slide 39: Thesis Proposal
Create simulation of channel
Evaluate which techniques increase covertness (while maximizing transmission rate)
Evaluate which detector(s) work best

## Slide 40: Detectors Available to Willie
Wideband Radiometer (Energy)
D’Agostino and Pearson’s Normal Test
Max Cut Detector (Cyclostationary)
Degree of Cyclostationarity (Cyclostationary)

## Slide 41: Detectors Available to Willie
✅ Wideband Radiometer (Energy)
✅ D’Agostino and Pearson’s Normal Test
✅ Max Cut Detector (Cyclostationary)
✅ Degree of Cyclostationarity (Cyclostationary)

## Slide 42: Protocols Available to Alice and Bob
Traditional:
  PSK
  FSK
  QAM
Spread Spectrum
  CDMA
  OFDM
  FH-CSS
Chaotic
  Chaotic Multi-Tone (CMT)
  Differential Chaos Shift Keying (DCSK)
  FH-OFDM-DCSK
Other
  QS-DS-CDMA

## Slide 43: Protocols Available to Alice and Bob
Traditional:
  ✅ PSK
  ✅ FSK
  ✅ QAM
Spread Spectrum
  ✅ CDMA
  ✅ OFDM
  FH-CSS
Chaotic
  Chaotic Multi-Tone (CMT)
  ✅ Differential Chaos Shift Keying (DCSK)
  ✅ FH-OFDM-DCSK
Other
  QS-DS-CDMA

## Slide 44: Questions?

## Slide 45: OFDM
Multiplex bits across orthogonal subcarriers
Flattens frequency spectrum
Helps mitigate FSF

## Slide 46: Chaotic Multi Tone
Chaotically select tone groups to transmit information
Signal is very random

## Slide 47: FH-OFDM-DCSK
Frequency Hopped OFDM Differential Chaos Shift Keying

## Slide 48: When Willie Doesn’t Know When
Alice picks one slot out of T(n) slots
She can transmit O(√n log(T(n))) bits
Willie has to monitor every slot.